## Slide 1: Operating Systems
Introduction to make an OS :
A Simple Operating System

## Slide 2: Goals of Our Simple OS
APIs for device access
  Read from the keyboard
  Read and write to a simple disk
  Display text to the screen
Ability to run a simple user program
A basic command line for running programs
32-bit x86
  IA32

## Slide 3: x86 Registers (32 bit)
General purpose registers
  EAX, EBX, ECX, EDX
  Used for pretty much anything
Stack registers
  ESP: Points to the top of the stack
    The stack grows down, so this is the lowest address
  EBP: Points to the bottom of the current stack frame
    Not strictly necessary, may be used as a general purpose register
Other registers
  EIP: Points to the currently executing instruction
  EFLAGS: Bit vector of flags
    Stores things like carry (after addition), equals zero (after a comparison), etc.

## Slide 4: Register Layout
x86 has gone through 16, 32, and 64 bit versions
Registers can be addressed in whole or in part
RAX
EAX
AX
AH
AL
64 bits
32 bits
16 bits
8 bit high and low

## Slide 5: x86 Assembly Examples
mov eax, 0x00ABCDE ; move 32-bit value to EAX
mov ax, 0xABCD ; move 16-bit value to AX
mov ah, 0xAB
mov al, 0xCD ; 3) + 4) are equivalent to 2)
add eax, ebx ; result stored in EAX
mov edx, [esp] ; dereference the pointer in ESP, move the value to EDX

## Slide 6: Important x86 Instructions
Instructions | Description | Examples
mov | Move data from one place to another | mov eax, 7 mov edx, [0xF0FF] mov [ebx], eax
add / sub | Add / subtract values in registers | add eax, ebx
inc / dec | Increment / decrement the value in a register | inc eax
call | Push EIP onto the stack and jump to a function | call 0x80FE4C
ret | Pop the top of the stack into EIP | ret
push / pop | Add or remove items to the stack | push eax
int | Execute the given interrupt handler | int 0x80
jmp | Load the given value into EIP | jmp 0x80FE4C
cmp | Compare the value of two registers and store the value in the flags register | cmp ebx, edx
jxx | Load the given value into EIP if the condition is met | jz 0x80FE4C jnz 0x80FE4C
In Intel assembly syntax, [] means dereference (e.g. *ptr in C)
Basics
Func.
Stack
Control Flow

## Slide 7: Typical Memory Layout
Example: 64KB of memory
  216 bytes
  Addresses from 0 to 65535
Not all memory is free
  Specific ranges get used by devices, system services, the BIOS, etc.
Memory mapped devices
Free Memory
BIOS Code
Interrupt Vector
0x0000
0x00FF
0x0DFF
0xF000
0xFFFF
Top
Bottom

## Slide 8: Memory Addressing
Address | Value
0xC7 | 0x00
0xC6 | 0x00
0xC5 | 0x10
0xC4 | 0x05
0xC3 | 0x00
0xC2 | ‘c’
0xC1 | ‘b’
0xC0 | ‘a’
mov ah, [0xC0] ; AH = ‘a’
mov ax, [0xC4] ; AX = 0x0510
Memory can be addressed as:
  Individual bytes
  Multi-byte words, double words, quad words, etc.

## Slide 9
10
Byte ordering
How to order bytes within multi-byte word in memory
Conventions
– (most) Sun’s, IBMs are “Big Endian” machines
• Least significant byte has highest address (comes last)
– (most) Intel’s are “Little Endian” machines
• Least significant byte has lowest address (comes first)
Example
– Variable x has 4-byte representation 0x01234567
– Address given by &x is 0x100

## Slide 10
11
Reading byte-reversed Listings
For most programmers, these issues are invisible
Except with networking or disassembly
– Text representation of binary machine code
– Generated by program that reads the machine code
Example fragment
Address
8048365:
8048366:
804836c:
Instruction Code
5b
81 c3 ab 12 00 00
83 bb 28 00 00 00 00
Assembly Rendition
pop %ebx
add $0x12ab,%ebx
cmpl $0x0,0x28(%ebx)
Deciphering Numbers
– Value:
– Pad to 4 bytes:
– Split into bytes:
– Reverse:
0x12ab
0x000012ab
00 00 12 ab
ab 12 00 00

## Slide 11: I/O Port Example
Output
mov eax, 1
mov dx, 0x3F8
start: out dx, al
inc eax
cmp eax, 32
jne start
…
Input
mov ebx, 0
mov dx, 0x3F8
start: in dx, ax
mov [esp + ebx], ax
inc ebx
cmp ebx, 31
jle start
…
Assume there is a serial port attached to port 0x3F8

## Slide 12: Memory Mapped Devices
RAM shared by the CPU and a device
Example: Console frame buffer
  Address range of 1920 bytes
  Corresponds to 24 lines of text, 80 characters wide
  CPU writes characters into the memory range…
  … Video hardware displays them on the screen
Address | Value
0xC2 | ‘e’
0xC1 | ‘h’
0xC0 | ‘T’

## Slide 13: Example Keyboard Controller
Simple, memory mapped keyboard interface
  2 bytes: keycode byte and status byte
When a key is pressed:
  The keycode byte is set to the character
  The status byte is set to 1
When the key is read:
  CPU sets the status byte to 0
Address | Purpose
0xF801 | keycode
0xF800 | status

## Slide 14: Sample Program 1 – Hello World
Writes “Hello World” to the frame buffer
Then loops forever
l
l
o
W
o
r
l
d
e
H
EBX
ECX
EDX
EAX
0xF000
H
11
H
He
Hel
Hell
Hello
Hello W
Hello Wo
Hello Wor
Hello Worl
Hello World
10
e
0xF001
9
l
0xF001
0xF002
0xF003
8
0xF004
7
o
0xF005
6
0xF006
5
W
0xF007
4
o
0xF008
3
r
0xF009
2
l
0xF00A
1
d
0xF00B
0
fbuf = 0xF000
str: 'Hello World'
begin: mov eax, str
mov ebx, 11
mov ecx, 0xF000
loop: mov edx, byte [eax]
inc eax
mov [ecx], byte edx
inc ecx
sub ebx, 1
jnz_loop done: jmp done

## Slide 15: Sample Program 1 – Hello World
In this program, there is no OS
  Program interacts directly with hardware
This approach might be used for highly-constrained, low-cost environments
  Example: simple embedded devices
In a system like this, the program is usually written into read-only-memory (ROM) at the factory

## Slide 16: Sample Program 2 – Keyboard to Screen
Reads input from the keyboard and writes it to the frame buffer
framebuf = 0xF000
status = 0xF800
keycode = 0xF801
begin: mov eax, 0xF000
loop: mov ebx, byte [0xF800]
cmp ebx, 0
jz loop
mov ebx, byte [0xF801]
mov [eax], byte ebx
inc eax
mov [0xF800], 0
jmp loop
How can we turn this functionality into an API?

## Slide 17: The x86 Stack
x86 CPU uses ESP register to implement a push down stack
Examples:
  push 0x01
  pop eax ; EAX = 1
Memory
0xCAFE | 0xAE
0x01 | 0xAA
 | 0xA6
 | 0xA2
 | 0x9E
 | 0x9A
 | 0x96
 | 0x92
 | 0x8E
 | 0x8A
 | 0x86
ESP

## Slide 18: Function Calls and the Stack
The stack is used to implement function calls
  call addr: call a function
    Calculates a return address (the address of the instruction following call)
    Pushes the return address on to the stack
    Jumps to addr (EIP = addr)
  ret: return from a function
    Pops the return address from the stack
    Jumps to the return address

## Slide 19: Function Call Example
…
10. push 2
11. push 1
12. call add
13. mov ecx, eax
…
20. add: mov eax, [esp + 4]
21. mov ebx, [esp + 8]
22. add eax, ebx
23. ret
Memory
0xCAFE | 0xAE
0x02 | 0xAA
0x01 | 0xA6
13 | 0xA2
 | 0x9E
ESP
EIP
Suppose we have code that calls
i = add(1, 2);

## Slide 20: Argument Ordering and Return Values
Function arguments are always pushed in reverse order
  Why?
  To support functions with a variable number of arguments
  Example: printf(“%i %f %s”, a, pi, str);
    Argument 1 tells you how many more arguments there are on the stack
By convention, return values are always placed in EAX
  This is why (typical) functions may only return one value

## Slide 21: Pop Quiz
…
27. call f
…
59. f: mov eax, [esp + 4]
…
Memory
10 | 0xAE
7 | 0xAA
28 | 0xA6
 | 0xA2
 | 0x9E
What does the stack look like after calling f(7, 10)?

## Slide 22: A Minimal Operating System
We’ll now write a simple OS that can:
  Read keyboard input
  Write it to the frame buffer
getkey()
  Loops until a key has been pressed
  Loads the key into EAX
getkey: mov edx, byte [status]
cmp edx, 0
jz getkey
mov [status], 0
mov eax, byte [keycode]
ret

## Slide 23: putchar()
putchar()
  Writes the 2 byte function argument to the frame buffer
  Maintains the frame buffer cursor
bufptr: variable holding a pointer to the frame buffer
putchar: mov eax, word [esp+ 4] mov ebx, dword [bufptr] mov [ebx], word eax add ebx, 1 mov [bufptr], ebx ret

## Slide 24: Using getkey() and putchar()
We can now rewrite Sample Program 2 using our simple OS
loop: call getkey push eax call putchar pop eax jmp loop
framebuf = 0xF000
status = 0xF800
keycode = 0xF801
begin: mov eax, 0xF000
loop: mov ebx, byte [0xF800]
cmp ebx, 0
jz loop
mov ebx, byte [0xF801]
mov [eax], byte ebx
inc eax
jmp loop
Old Code
New Code

## Slide 25: Why Do We Care?
Reusability
  Many programs can use getkey() and putchar()
Abstraction
  Programs don’t need to know details of the keyboard and frame buffer interfaces
Portability
  Program could run on another OS that supports getkey() and putchar()…
  … even if the hardware interface has changes

## Slide 26: Let’s Build a Basic Shell
Almost all OSes include a shell
  A program that takes commands from the user
  Earliest (and best) shells were command lines
  Modern shells are GUIs
Let’s build a shell into our OS
  Read a command line from the keyboard
  Read the associated program from the disk
  Load the program into memory and execute it

## Slide 27: Basic Program Loading
Memory regions are reserved
  Memory mapped hardware
  OS code
  IVT
  Etc…
To load and run a program:
  Read the program from disk into the program region of memory
  Use call to jump to the first instruction of the program
    Called the entry point
IVT
0x0000
0xFFFF
Main Memory
getchar()
User Program Region
Hardware
OS Code
putchar()

## Slide 28: Example Disk Controller
Disk drive interface
  Reads and writes occur in 512-byte blocks
  Block numbers start at 0
To write to block B
  Copy the data into range 0xF900 – 0xFAFF
  Write B to 0xF822
  Write ‘W’ to 0xF820
    Tells the drive to write the buffer
  Drive will write 0 to 0xF820 when the transfer is complete
Address | Purpose
0xFAFF | 512-byte buffer
… | 
0xF900 | 
0xF822 | block address
0xF820 | cmd/status

## Slide 29: Example Disk Controller (cont.)
To read from block B
  Write B to 0xF822
  Write ‘R’ to 0xF820
    Tells the drive to read data from the disk into the buffer
  Drive will write 0 to 0xF820 when the transfer is complete
  Data from B is now available in 0xF900 – 0xFAFF
Address | Purpose
0xFAFF | 512-byte buffer
… | 
0xF900 | 
0xF822 | block address
0xF820 | cmd/status

## Slide 30: Additional OS APIs
Assume we have already implemented some functions
  read_disk_block() reads a block from the disk to some address in memory
  getline() reads a line from the keyboard and stores it into a buffer

## Slide 31: Basic File System
Assume the disk is divided into blocks
We introduce a trivial file system
  Block 0 is the directory mapping of the file system
  Other blocks are program data blocks
Valid? | Name | Addr | len
1 | “file1.txt” | 1 | 2
0 |  |  | 
1 | “program.com” | 3 | 3
Block 0 (directory)
file1.txt
Blocks 1 and 2
program.com
Blocks 3, 4 and 5

## Slide 32: File System Structures
struct dirent {
bool valid;
char name[16]; int start; int len;
};
struct dirent directory[BLK_SIZ/sizeof(struct dirent)]
read_disk_block(/*blk #*/ 0, /*destination*/ directory);
Valid? | Name | Addr | len
1 | “file1.txt” | 1 | 2
0 |  |  | 
1 | “program.com” | 3 | 3
Block 0 (directory)
file1.txt
Blocks 1 and 2
program.com
Blocks 3, 4 and 5

## Slide 33: Basic Command Line
We can now write a very simple command line:
char buffer[80]; struct dirent directory[NDIR];
int i, start, count;
void *program_base = …; /* probably 0x100 or so */
while (1) {
getline(buffer);
read_disk_block(DIR_SECTOR, directory);
for (i = 0; i < NDIR; i++) {
if (strcmp(buffer,directory[i].name)== 0 && directory[i].valid) {
for (j = 0; j < directory[i].len; j++)
read_disk_block(/* block # */ directory[i].start + j, /* destination*/ program_base + j * 512);
break;
}
}
asm(“call program_base”);
/* returns here when program is done */
}

## Slide 34: Limitations of Our OS
Crashes if it can’t find the specified program
If the program crashes, the whole OS needs to be restarted
Programs may not run if the OS is upgraded
  Why?
  Programs access OS APIs directly
  What if the addresses change?
IVT
0x0000
0xFFFF
Main Memory
Hardware
getchar()
OS Code
putchar()
User Program

## Slide 35: Similarities with MS-DOS 1.0
Separate OS and program spaces
System call table accessed via interrupt
Command line is part of OS
Similar keyboard controller, frame buffer, and disk controller
IVT
0x0000
Top
Main Memory
MS-DOS
BIOS
User Program Region