## Slide 1: Operating Systems
Virtual Memory - I

## Slide 2: Physical vs. Virtual Memory
Clearly, physical memory has limitations
  No protection or isolation
  Fixed pointer addresses
  Limited size
  Etc.
Virtualization can solve these problems!
  As well as enable additional, cool features

## Slide 3: Protection and Isolation
Physical memory does not offer protection or isolation
0x00000000
0xFFFFFFFF
Kernel Memory
Process 1
w/ Secret Data
Physical Memory
Evil Process
I’m in your process, stealing your data ;)
Oh sorry, I didn’t mean to overwrite your task_structs ;)

## Slide 4: Problem: Pointers in Programs
Consider the following code:
int foo(int a, int b) { return a *b – a / b; }
int main(void) { return foo(10, 12); }
Compiled, it might look like this:
000FE4D8 <foo>:
000FE4D8: mov eax, [esp+4]
000FE4DB: mov ebx, [esp+8]
000FE4DF: mul eax, ebx
…
000FE21A: push eax
000FE21D: push ebx
000FE21F: call 0x000FE4D8
… but this assembly assumes foo() is at address 0x000FE4D8

## Slide 5: Compilation and Program Loading
Compiled programs include fixed pointer addresses
Example:
000FE4D8 <foo>:
…
000FE21A: push eax
000FE21D: push ebx
000FE21F: call 0x000FE4D8
Problem: what if the program is not loaded at corresponding address?
0x00000000
0xFFFFFFFF
Kernel Memory
Process 1
Physical Memory
Process 2
Addr of foo(): 0x000FE4D8
Addr of foo(): 0x0DEB49A3

## Slide 6: Physical Memory has Limited Size
RAM is cheap, but not as cheap as solid state or cloud storage
What happens when you run out of RAM?
0x00000000
0xFFFFFFFF
Kernel Memory
Process 1
Process 2
Process 3
Process 4
Process 5

## Slide 7: Program Load Addresses
Loader must place each process in memory
Program may not be placed at the correct location!
  Example: two copies of the same program
0xFFFFFFFF
0x00000000
Code
Heap
Stack
Process 1
Code
Heap
Stack
Process 2
Addr of foo(): 0x000FE4D8
Addr of foo(): 0x0DEB49A3

## Slide 8: Address Spaces for Multiple Processes
Many features of processes depend on pointers
  Addresses of functions
  Addresses of strings, data
  Etc.
For multiple processes to run together, they all have to fit into memory together
However, a process may not always be loaded into the same memory location
0xFFFFFFFF
0x00000000
Code
Heap
Stack
Process 2
Code
Heap
Stack
Process 1
Code
Heap
Stack
Process 3

## Slide 9: Address Spaces for Multiple Processes
There are several methods for configuring address spaces for multiple processes
  Fixed address compilation
  Load-time fixup
  Position independent code
  Hardware support

## Slide 10: Fixed-Address Compilation
Single Copy of Each Program
Compile each program once, with fixed addresses
OS may only load program at the specified offset in memory
Typically, only one process may be run at any time
Example: MS-DOS 1.0
Multiple Copies of Each Program
Compile each program multiple times
Once for each possible starting address
Load the appropriate compiled program when the user starts the program
Bad idea
  Multiple copies of the same program

## Slide 11: Load-Time Fixup
Calculate addresses at load-time instead of compile-time
The program contains a list of locations that must be modified at startup
  All relative to some starting address
Used in some OSes that run on low-end microcontrollers without virtual memory hardware
Program
0x000 CALL xxx
  ...
  0x300 ...
000: xxx=+300
Fix-up information
After loading
0x200 CALL 0x500
  ...
0x500 ...

## Slide 12: Position-Independent Code
Compiles programs in a way that is independent of their starting address
  PC-relative address (PC=IP)
Slightly less efficient than absolute addresses
Commonly used today for security reasons
PC-relative addressing
Absolute addressing
0x200 CALL 0x500 ...
0x500 ...
0x200 CALL IP+0x300
  ...
0x500 ...

## Slide 13: Hardware Support
Hardware address translation
Most popular way of sharing memory between multiple processes
  Linux
  OS X
  Windows
Program is compiled to run at a fixed location in virtual memory
The OS uses the MMU to map these locations to physical memory

## Slide 14: Virtual memory
What do we mean by virtual memory?
  Processes use virtual (or logical) addresses
  Virtual addresses are translated to physical addresses
0x0000
0xFFFF
Kernel Memory
Process 1
Physical Memory
(Reality)
Process’ View of
Virtual Memory
0x0000
0xFFFF
Process 2
Process 3
Process 1
All the memory belongs to me!
I am master of all I survey!
Physical Address
Virtual Address
Magical Address Translation Black Box

## Slide 15: MMU and Virtual Memory
The Memory Management Unit (MMU) translates between virtual addresses and physical addresses
  Process uses virtual address for calls and data load/store
  MMU translates virtual addresses to physical addresses
  The physical addresses are the true locations of code and data in RAM

## Slide 16: Implementing Address Translation
In a system with virtual memory, each memory access must be translated
Modern systems have hardware support that facilitates address translation
  Implemented in the Memory Management Unit (MMU) of the CPU
  Cooperates with the OS to translate virtual addresses into physical addresses

## Slide 17: Virtual Memory Implementations
There are many ways to implement an MMU
  Base and bound registers
  Segmentation
  Page tables
  Multi-level page tables
We will discuss each of these approaches
Old, simple, limited functionality
Modern, complex, lots of functionality

## Slide 18: Base and bounds registers

## Slide 19: Base and Bounds Registers
A simple mechanism for address translation
Maps a contiguous virtual address region to a contiguous physical address region
0x0000
0xFFFF
Kernel Memory
Process 1
Physical Memory
0x00FF
0x10FF
Process 1
Process’ View of
Virtual Memory
0x0001
0x1001
Register | Value
EIP | 0x0023
ESP | 0x0F76
BASE | 0x00FF
BOUND | 0x1000

## Slide 20: Base and Bounds Example
0x0000
0xFFFF
Kernel Memory
Process 1
Physical Memory
0x00FF
0x10FF
Process 1
Process’ View of
Virtual Memory
0x0001
0x1001
Register | Value
EIP | 0x0023
ESP | 0x0F76
BASE | 0x00FF
BOUND | 0x1000
0x0023 mov eax, [esp]
1) Fetch instruction
0x0023 + 0x00FF = 0x0122
2) Translate memory access
0x0F76 + 0x00FF = 0x1075
3) Move value to register
[0x1075]  eax
1
2
1
2

## Slide 21: Protection and Isolation
0x0000
0xFFFF
Kernel Memory
Process 1
Physical Memory
0x00FF
0x10FF
Process 1
Process’ View of
Virtual Memory
0x0001
0x1001
Register | Value
EIP | 0x0023
ESP | 0x0F76
BASE | 0x00FF
BOUND | 0x1000
0x0023 mov eax, [0x4234]
1) Fetch instruction
0x0023 + 0x00FF = 0x0122
2) Translate memory access
0x4234 + 0x00FF = 0x4333
0x1333 > 0x10FF
(BASE + BOUND)
Raise Protection Exception!
1
2
1
2

## Slide 22: Implementation Details
BASE and BOUND are protected registers
  Only code in Ring 0 may modify BASE and BOUND
  Prevents processes from modifying their own sandbox
Each CPU has one BASE and one BOUND register
  Just like ESP, EIP, EAX, etc…
  Thus, BASE and BOUND must be saved a restored during context switching

## Slide 23: Base and Bound Pseudocode
PhysAddr = VirtualAddress + BASE
if (PhysAddr >= BASE + BOUND)
RaiseException(PROTECTION_FAULT)
Register = AccessMemory(PhysAddr)

## Slide 24: Advantages of Base and Bound
Simple hardware implementation
Simple to manage each process’ virtual space
Processes can be loaded at arbitrary fixed addresses
Offers protection and isolation
Offers flexible placement of data in memory
0x00000000
0xFFFFFFFF
Kernel Memory
Process 1
Physical Memory
Process 2
I’m loaded at address 0x00AF
No, I’m loaded at address 0x00AF
Previous BASE  0x00FF
New BASE  0x10A0

## Slide 25: Limitations of Base and Bound
Processes can overwrite their own code
  Processes aren’t protected from themselves
No sharing of memory
  Code (read-only) is mixed in with data (read/write)
Process memory cannot grow dynamically
  May lead to internal fragmentation
0x00000000
0xFFFFFFFF
Kernel Memory
/bin/bash
Physical Memory
/bin/bash
Code
Code
Data
Data
Code is duplicated in memory :(

## Slide 26: Internal Fragmentation
BOUND determines the max amount of memory available to a process
How much memory do we allocate?
  Empty space leads to internal fragmentation
What if we don’t allocate enough?
  Increasing BOUND after the process is running doesn’t help
Physical Memory
Code
Heap
Stack
Wasted space = internal fragmentation
Heap
Stack
Increasing BOUND doesn’t move the stack away from the heap

## Slide 27: Segmentation

## Slide 28: Towards Segmented Memory
Having a single BASE and a single BOUND means code, stack, and heap are all in one memory region
  Leads to internal fragmentation
  Prevents dynamically growing the stack and heap
Segmentation is a generalization of the base and bounds approach
  Give each process several pairs of base/bounds
    May or may not be stored in dedicated registers
  Each pair defines a segment
  Each segment can be moved or resized independently

## Slide 29: Segmentation Details
The code and data of a process get split into several segments
  3 segments is common: code, heap, and stack
  Some architectures support >3 segments per process
Each process views its segments as a contiguous region of memory
  But in physical memory, the segments can be placed in arbitrary locations
Question: given a virtual address, how does the CPU determine which segment is being addressed?

## Slide 30: Segments and Offsets
Key idea: split virtual addresses into a segment index and an offset
Example: suppose we have 14-bit addresses
  Top 2 bits are the segment
  Bottom 12 bits are the offset
4 possible segments per process
  00, 01, 10, 11
13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Segment
Offset

## Slide 31: Separation of Responsibility
The OS manages segments and their indexes
  Creates segments for new processes in free physical memory
  Builds a table mapping segments indexes to base addresses and bounds
  Swaps out the tables and segment registers during context switches
  Frees segments from physical memory
The CPU translates virtual addresses to physical addresses on demand
  Uses the segment registers/segment tables built by the OS

## Slide 32: Segmentation Example
0x0000
0x3FFF
Process’ View of
Virtual Memory
Code
Segment | Index | Base | Bound
CS (Code) | 00 | 0x0020 | 0x0100
HS (Heap) | 01 | 0xB000 | 0x0100
SS (Stack) | 10 | 0x0400 | 0x0100
0x0023 mov eax, [esp]
1) Fetch instruction
0x0023 (EIP) - 00000000100011
0x0020 (CS) + 0x0023 = 0x0043
2) Translate memory access
0x2015 (ESP) – 10000000010101
0x0400 (SS) + 0x0015 = 0x0415
0x1000
0x0000
0xFFFF
Kernel Memory
Physical Memory
Code
Heap
Stack
Code
Heap
Stack
0x0020
0xB100
0xB000
0x0120
0x0400
0x0500
0x2000
0x3000
Heap
Stack

## Slide 33: Segmentation Pseudocode
// get top 2 bits of 14-bit VA
Segment = (VirtualAddress & SEG_MASK) >> SEG_SHIFT
// now get offset
Offset = VirtualAddress & OFFSET_MASK
if (Offset >= Bounds[Segment])
RaiseException(PROTECTION_FAULT)
else
PhysAddr = Base[Segment] + Offset
Register = AccessMemory(PhysAddr)

## Slide 34: More on Segments
In the previous example, we use a 14-bit address space with 2 bits reserved for the segment index
  This limits us to 4 segments per process
  Each segment is 212 = 4KB in size
Real segmentation systems tend to have
  More bits for the segments index (16-bits for x86)
  More bits for the offset (16-bits for x86)
However, segments are course-grained
  Limited number of segments per process (typically ~4)

## Slide 35: Segment Permissions
Many CPUs (including x86) support permissions on segments
  Read, write, and executable
Disallowed operations trigger an exception
  E.g. Trying to write to the code segment
0x0000
0x3FFF
Process 1’s View of
Virtual Memory
Code
Index | Base | Bound | Permissions
00 | 0x0020 | 0x0100 | RX
01 | 0xB000 | 0x0100 | RW
10 | 0x0400 | 0x0100 | RW
11 | 0xE500 | 0x100 | R
0x1000
0x2000
0x3000
Heap
Stack
.rodata

## Slide 36: x86 Segments
Intel 80286 introduced segmented memory
  CS – code segment register
  SS – stack segment register
  DS – data segment register
  ES, FS, GS – extra segment registers
In 16-bit (real mode) x86 assembly, segment:offset notation is common
  mov [ds:eax], 42 // move 42 to the data segment, offset // by the value in eax
  mov [esp], 23 // uses the SS segment by default

## Slide 37: x86 Segments Today
Segment registers and their associated functionality still exist in today’s x86 CPUs
However, the 80386 introduced page tables
  Modern OSes “disable” segmentation
  The Linux kernel sets up four segments during bootup
Segment Name | Description | Base | Bound | Ring
KERNEL_CS | Kernel code | 0 | 4 GB | 0
KERNEL_DS | Kernel data | 0 | 4 GB | 0
USER_CS | User code | 0 | 4 GB | 3
USER_DS | User data | 0 | 4 GB | 3
Pages are used to virtualize memory, not segments
Used to label pages with protection levels

## Slide 38: What is a Segmentation Fault?
If you try to read/write memory outside a segment assigned to your process
Examples:
  char buf[5];
  strcpy(buf, “Hello World”);
  return 0; // why does it seg fault when you return?
Today “segmentation fault” is an anachronism
  All modern systems use page tables, not segments

## Slide 39: Shared Memory
0x0000
0x3FFF
Process 1’s View of
Virtual Memory
Code
Index | Base | Bound
00 | 0x0020 | 0x0100
01 | 0xB000 | 0x0100
10 | 0x0400 | 0x0100
11 | 0xE500 | 0x0300
0x1000
0x2000
0x3000
Heap
Stack
0x0000
0x3FFF
Process 2’s View of
Virtual Memory
0x1000
0x2000
0x3000
Code
Heap
Stack
Shared Data
Shared Data
Index | Base | Bound
00 | 0x0020 | 0x0100
01 | 0xC000 | 0x0100
10 | 0x0600 | 0x0100
11 | 0xE500 | 0x0300
Same 00 and 01 physical segments
Different 01 and 10 physical segments

## Slide 40: Advantages of Segmentation
All the advantages of base and bound
Better support for sparse address spaces
  Code, heap, and stack are in separate segments
  Segment sizes are variable
  Prevents internal fragmentation
Supports shared memory
Per segment permissions
  Prevents overwriting code, or executing data

## Slide 41: External Fragmentation
Problem: variable size segments can lead to external fragmentation
  Memory gets broken into random size, non-contiguous pieces
Example: there is enough free memory to start a new process
  But the memory is fragmented :(
Compaction can fix the problem
  But it is extremely expensive
Kernel Memory
Physical Memory
Code
Heap
Stack
Code
Heap
Stack
Heap
Stack
Code
Code
Heap
Stack
Code
Heap
Stack

## Slide 42: Paging

## Slide 43: Towards Paged Memory
Segments improve on base and bound, but they still aren’t granular enough
  Segments lead to external fragmentation
The paged memory model is a generalization of the segmented memory model
  Physical memory is divided up into physical pages (a.k.a. frames) of fixed sizes
  Code and data exist in virtual pages
  A table maps virtual pages  physical pages (frames)

## Slide 44: Toy Example
Suppose we have a 64-byte virtual address space
  Lets specify 16 bytes per page
How many bits do virtual addresses need to be in this system?
  26 = 64 bytes, thus 6 bit addresses
Page 0
0
64
16
32
48
Page 1
Page 2
Page 3
Virtual Memory
How many bits of the virtual address are needed to select the physical page?
  64 bytes / 16 bytes per page = 4 pages
  22 = 4, thus 2 bits to select the page
5 | 4 | 3 | 2 | 1 | 0
Virtual Page #
Offset

## Slide 45: Toy Example, Continued
Page 0
0
64
16
32
48
Page 1
Page 2
Page 3
Virtual Memory
Frame 0
0
64
16
32
48
Frame 1
Frame 2
Frame 3
Physical Memory
Frame 4
128
96
112
Frame 5
Frame 6
Frame 7
80
Virtual Page # | Physical Page #
00 (0) | 010 (2)
01 (1) | 111 (7)
10 (2) | 100 (4)
11 (3) | 001 (1)
mov eax, [21]
Translation
21 – 010101
117 – 1110101

## Slide 46: Concrete Example
Assume a 32-bit virtual and physical address space
  Fix the page size at 4KB (4096 bytes, 212)
How many total pages will there be?
  232 / 212 = 1048576 (220)
How many bits of a virtual address are needed to select the physical page?
  20 bits (since there are 1048576 total pages)
Assume that each page table entry is 4 bytes large
  How big will the page table be?
  1048586 * 4 bytes = 4MB of space
Each process needs its own page table
100 processes = 400MB of page tables

## Slide 47: Concrete Example, Continued
Process 1 requires:
  2 KB for code (1 page)
  7 KB for stack (2 pages)
  12 KB for heap (3 pages)
0
232
Process 1’s View of
Virtual Memory
Code
Heap
Stack
Heap
Heap
Stack
VPN | PFN | Valid?
0 … i - 1 | whatever | 0
i | d | 1
i + 1 … j – 1 | whatever | 0
j | b | 1
j + 1 | f | 1
j + 2 | e | 1
j + 3 … k - 1 | whatever | 0
k | a | 1
k + 1 | c | 1
Page i
Page j
Page j + 1
Page j + 2
Page k
Page k + 1
0
230
Kernel Memory
Physical Memory
Code
Heap
Stack
Heap
Heap
Stack
Frame a
Frame b
Frame c
Frame d
Frame e
Frame f
The vast majority of each process’ page table is empty, i.e. the table is sparse
Heap
Heap
Page j + 3
Frame g
Modify [ j+3, g, 1]

## Slide 48: Page Table Implementation
The OS creates the page table for each process
  Page tables are typically stored in kernel memory
  OS stores a pointer to the page table in a special register in the CPU (CR3 register in x86)
  On context switch, the OS swaps the pointer for the old processes table for the new processes table
The CPU uses the page table to translate virtual addresses into physical addresses

## Slide 49: x86 Page Table Entry
On x86, page table entries (PTE) are 4 bytes
31 - 12 | 11 - 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Page Frame Number (PFN) | Unused | G | PAT | D | A | PCD | PWT | U/S | W | P
Bits related to permissions
  W – writable bit – is the page writable, or read-only?
  U/S – user/supervisor bit – can user-mode processes access this page?
Hardware caching related bits: G, PAT, PCD, PWT
Bits related to swapping
  P – present bit – is this page in physical memory?
  A – accessed bit – has this page been read recently?
  D – dirty bit – has this page been written recently?
We will revisit these later in the lecture…

## Slide 50: Page Table Pseudocode
// Extract the VPN from the virtual address
VPN = (VirtualAddress & VPN_MASK) >> SHIFT
// Form the address of the page-table entry (PTE)
PTEAddr = PTBR + (VPN * sizeof(PTE))
// Fetch the PTE
PTE = AccessMemory(PTEAddr)
if (PTE.Valid == False) // Check if process can access the page
RaiseException(SEGMENTATION_FAULT)
else if (CanAccess(PTE.ProtectBits) == False)
RaiseException(PROTECTION_FAULT)
// Access is OK: form physical address and fetch it
offset = VirtualAddress & OFFSET_MASK
PhysAddr = (PTE.PFN << PFN_SHIFT) | offset
Register = AccessMemory(PhysAddr)

## Slide 51: Tricks With Permissions and Shared Pages
Recall how fork() is implemented
  OS creates a copy of all pages controlled by the parent
fork() is a slooooow operation
  Copying all that memory takes a looooong time
Can we improve the efficiency of fork()?
  Yes, if we are clever with shared pages and permissions!

## Slide 52: Copy-on-Write
Key idea: rather than copy all of the parents pages, create a new page table for the child that maps to all of the parents pages
  Mark all of the pages as read-only
  If parent or child writes to a page, a protection exception will be triggered
  The OS catches the exception, makes a copy of the target page, then restarts the write operation
Thus, all unmodified data is shared
  Only pages that are written to get copied, on demand

## Slide 53: Copy-on-Write Example
0
230
Kernel Memory
Physical Memory
Code
Heap
Stack
Frame a
Frame d
Frame f
Function | VPN | PFN | Writable?
Code | i | d | 0
Heap | j | b | 1
Stack | k | a | 1
Parents Page Table
Function | VPN | PFN | Writable?
Code | i | d | 0
Heap | j | b | 0
Stack | k | a | 0
Childs Page Table
0
0
Protection Exception
Stack
Frame m
1
1
Stack
m
Write
Write
Write

## Slide 54: Advantages of Page Tables
All the advantages of segmentation
Even better support for sparse address spaces
  Each page is relatively small
  Fine-grained page allocations to each process
  Limits internal fragmentation
All pages are the same size
  Each to keep track of free memory (say, with a bitmap)
  Prevents external fragmentation
Per page permissions
  Prevents overwriting code, or executing data

## Slide 55: Problems With Page Tables
Page tables are huge
  On a 32-bit machine with 4KB pages, each process’ table is 4MB
  On a 64-bit machine with 4KB pages, there are 252 entries per table  252 * 4 bytes = 16PB
  And the vast majority of entries are empty/invalid!
Page table indirection adds significant overhead to all memory accesses

## Slide 56: Page Tables are Slow
0x1024 mov [edi + eax * 4], 0x0
0x1028 inc eax
0x102C cmp eax, 0x03E8
0x1030 jne 0x1024
How many memory accesses occur during each iteration of the loop?
  4 instructions are read from memory
  [edi + eax * 4] writes to one location in memory
  5 page table lookups
    Each memory access must be translated
    … and the page tables themselves are in memory
Naïve page table implementation doubles memory access overhead

## Slide 57: Locality is the rescue: TLB

## Slide 58: Problem: Page Table Speed
Page tables give us a great deal of flexibility and granularity to implement virtual memory
However, page tables are large, thus they must go in RAM (as opposed to in a CPU register)
  Each virtual memory access must be translated
  Each translation requires a table lookup in memory
  Thus, memory overhead is doubled
How can we use page tables without this memory lookup overhead?

## Slide 59: Caching
Key idea: cache page table entries directly in the CPU’s MMU
  Translation Lookaside Buffer (TLB)
   address translation cache
TLB stores recently used PTEs
  Subsequent requests for the same virtual page can be filled from the TLB cache
Directly addresses speed issue of page tables
  On-die CPU cache is very, very fast
  Translations that hit the TLB don’t need to be looked up from the page table in memory

## Slide 60: Example TLB Entry
VPN & PFN – virtual and physical pages
G – is this page global (i.e. accessible by all processes)?
ASID – address space ID
  D – dirty bit – has this page been written recently?
  V – valid bit – is this entry in the TLB valid?
  C – cache coherency bits – for multi-core systems
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
ASID
G
Virtual Page Number (VPN)
V
D
C
Physical Frame Number (PFN)
More on this later…

## Slide 61: TLB Control Flow Psuedocode
VPN = (VirtualAddress & VPN_MASK) >> SHIFT
(Success, TlbEntry) = TLB_Lookup(VPN)
if (Success == True) // TLB Hit
if (CanAccess(TlbEntry.ProtectBits) == True)
Offset = VirtualAddress & OFFSET_MASK
PhysAddr = (TlbEntry.PFN << SHIFT) | Offset
AccessMemory(PhysAddr)
else
RaiseException(PROTECTION_FAULT)
else // TLB Miss
PTEAddr = PTBR + (VPN * sizeof(PTE))
PTE = AccessMemory(PTEAddr)
if (PTE.Valid == False)
RaiseException(SEGMENTATION_FAULT)
else if (CanAccess(PTE.ProtectBits) == False)
RaiseException(PROTECTION_FAULT)
TLB_Insert(VPN, PTE.PFN, PTE.ProtectBits)
RetryInstruction()
Load the page table entry from memory, add it to the TLB, and retry
Make sure we have permission, then proceed
Fast Path
Slow Path

## Slide 62: Reading an Array (no TLB)
Assuming no hardware caching
Suppose we have a 10KB array of integers
  Assume 4KB pages
With no TLB, how many memory accesses are required to read the whole array?
  10KB / 4 = 2560 integers in the array
  Each requires one page table lookup, one memory read
  5120 reads, plus more for the instructions themselves

## Slide 63: Reading an Array (with TLB)
Same example, now with TLB
  10KB integer array
  4KB pages
  Assume the TLB starts off cold (i.e. empty)
How many memory accesses to read the array?
  2560 to read the integers
  3 page table lookups
  2563 total reads
  TLB hit rate: 99.88%
Process 1’s View of
Virtual Memory
Array Data
Array Data
Array Data
Page j
Page j + 1
Page j + 2
VPN | PFN
j | a
j + 1 | b
j + 2 | c
TLB

## Slide 64: Locality
TLB, like any cache, is effective because of locality
  Spatial locality: if you access memory address x, it is likely you will access x + 1 soon
    Most of the time, x and x + 1 are in the same page
  Temporal locality: if you access memory address x, it is likely you will access x again soon
    The page containing x will still be in the TLB, hopefully

## Slide 65: Be Careful With Caching
Recall: TLB entries have an ASID (address space ID) field. What is this for?
  Here’s a hint: think about context switching
VPN | PFN
i | d
j | b
k | a
Process 1’s Page Table
VPN | PFN
i | r
j | u
k | s
Process 2 Page Table
VPN | PFN
i | d
J | b
k | a
TLB
VPNs are the same, but PFN mappings have changed!
Problem: TLB entries may not be valid after a context switch

## Slide 66: Potential Solutions
Clear the TLB (mark all entries as invalid) after each context switch
  Works, but forces each process to start with a cold cache
  Only solution on x86 (until ~2008)
Associate an ASID (address space ID) with each process
  ASID is just like a process ID in the kernel
  CPU can compare the ASID of the active process to the ASID stored in each TLB entry
  If they don’t match, the TLB entry is invalid

## Slide 67: Replacement Policies
On many CPUs (like x86), the TLB is managed by the hardware
Problem: space in the TLB is limited (usually KB)
  Once the TLB fills up, how does the CPU decide what entries to replace (evict)?
Typical replacement policies:
  FIFO: easy to implement, but certain access patterns result in worst-case TLB hit rates
  Random: easy to implement, fair, but suboptimal hit rates
  LRU (Least Recently Used): algorithm typically used in practice

## Slide 68: Hardware vs. Software Management
Thus far, discussion has focused on hardware managed TLBs (e.g. x86)
  PTE = AccessMemory(PTEAddr)
  TLB_Insert(VPN, PTE.PFN, PTE.ProtectBits)
  CPU dictates the page table format, reads page table entries from memory
  CPU manages all TLB entries
However, software managed TLBs are also possible (e.g. MIPS and SPARC)

## Slide 69: Software Managed TLB Pseudocode
VPN = (VirtualAddress & VPN_MASK) >> SHIFT
(Success, TlbEntry) = TLB_Lookup(VPN)
if (Success == True) // TLB Hit
if (CanAccess(TlbEntry.ProtectBits) == True)
Offset = VirtualAddress & OFFSET_MASK
PhysAddr = (TlbEntry.PFN << SHIFT) | Offset
Register = AccessMemory(PhysAddr)
else
RaiseException(PROTECTION_FAULT)
else // TLB Miss
RaiseException(TLB_MISS)
The hardware does not:
Try to read the page table
Add/remove entries from the TLB

## Slide 70: Implementing Software TLBs
Key differences vs. hardware managed TLBs
  CPU doesn’t insert entries into the TLB
  CPU has no ability to read page tables from memory
On TLB miss, the OS must handle the exception
  Locate the correct page table entry in memory
  Insert the PTE into the TLB (evict if necessary)
  Tell the CPU to retry the previous instruction
Note: TLB management instructions are privileged
  Only the kernel can modify the TLB

## Slide 71: Comparing Hardware and Software TLBs
Hardware TLB
Advantages
  Less work for kernel developers, CPU does a lot of work for you
Disadvantages
  Page table data structure format must conform to hardware specification
  Limited ability to modify the CPUs TLB replacement policies
Software TLB
Advantages
  No predefined data structure for the page table
  OS is free to implement novel TLB replacement policies
Disadvantages
  More work for kernel developers
  Beware infinite TLB misses!
    OSes page fault handler must always be present in the TLB
Greater flexibility
Easier to program

## Slide 72: Advanced page tables

## Slide 73: Problem: Page Table Size
At this point, we have solved the TLB speed issue
However, recall that pages tables are large and sparse
  Example: 32-bit system with 4KB pages
  Each page table is 4MB
  Most entries are invalid, i.e. the space is wasted
How can we reduce the size of the page tables?
  Many possible solutions
  Multi-layer page tables are most common (x86)

## Slide 74: Simple Solution: Bigger Pages
Suppose we increase the size of pages
  Example: 32-bit system, 4MB pages
  232 / 222 = 1024 pages per process
  1024 * 4 bytes per page = 4KB page tables
What is the drawback?
  Increased internal fragmentation
  How many programs actually have 4MB of code, 4MB of stack, and 4MB of heap data?

## Slide 75: Alternate Data Structures
Thus far, we’ve assumed linear page tables
  i.e. an array of page table entries
What if we switch to an alternate data structure?
  Hash table
  Red-black tree
Why is switching data structures not always feasible?
  Can be done of the TLB is software managed
  If the TLB is hardware managed, then the OS must use the page table format specified by the CPU

## Slide 76: Inverted Page Tables
Our current discussion focuses on tables that map virtual pages to physical pages
What if we flip the table: map physical pages to virtual pages?
  Since there is only one physical memory, we only need one inverted page table!
VPN | PFN
i | d
j | b
k | a
VPN | PFN
i | r
j | u
k | s
VPN | PFN
i | r
j | u
k | s
PFN | VPN
i | d
j | b
k | a
Standard page tables: one per process
Inverted page tables: one per system
Traditional Tables
Inverted Table

## Slide 77: Normal vs. Inverted Page Tables
Advantage of inverted page table
  Only one table for the whole system
Disadvantages
  Lookups are more computationally expensive
  How to implement shared memory?
VPN | PFN
i | d
j | b
k | a
PFN | VPN
i | d
j | b
k | a
VPN serves as an index into the array, thus O(1) lookup time
Traditional Table
Inverted Table
Table must be scanned to locate a given VPN, thus O(n) lookup time

## Slide 78: Multi-Level Page Tables
Key idea: split the linear page table into a tree of sub-tables
  Benefit: branches of the tree that are empty (i.e. do not contain valid pages) can be pruned
Multi-level page tables are a space/time tradeoff
  Pruning reduces the size of the table (saves space)
  But, now the tree must be traversed to translate virtual addresses (increased access time)
Technique used by modern x86 CPUs
  32-bit: two-level tables
  64-bit: four-level tables

## Slide 79: Multi-Level Table Toy Example
Imagine a small, 16KB address space
  64-byte pages, 14-bit virtual addresses, 8 bits for the VPN and 6 for the offset
How many entries does a linear page table need?
  28 = 256 entries
0
214
Process 1’s View of
Virtual Memory
Stack
Heap
Code
Page 0
Page 4
Page 255
Assume 3 pages out of 256 total pages are in use

## Slide 80: From Linear to Two-levels Tables
How do you turn a linear table into a multi-level table?
  Break the linear table up into page-size units
256 table entries, each is 4 bytes large
  256 * 4 bytes = 1KB linear page tables
Given 64-byte pages, a 1KB linear table can be divided into 16 64-byte tables
  Each sub-table holds 16 page table entries
13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Virtual Page #
Offset
Page Directory Index
(Table Level 1)
Page Table Index
(Table Level 2)

## Slide 81
VPN | PFN | Valid?
00000000 | a | 1
... |  | 0
00000100 | b | 1
… |  | 0
11111111 | c | 1
Linear Page Table
0
214
Process 1’s View of
Virtual Memory
Stack
Heap
Code
Page 0
Page 4
Page 255
13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Offset
Virtual Page Number
253 tables entries are empty, space is wasted :(

## Slide 82
0
214
Process 1’s View of
Virtual Memory
Stack
Heap
Code
Page 0
Page 4
Page 255
13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Offset
Page Directory
Index
Page Table
Index
Index | PFN | Valid?
0000 | a | 1
… |  | 0
0100 | b | 1
… |  | 0
Page Table 0000
Index | PFN | Valid?
0000 |  | 0
… |  | 0
1111 | c | 1
Page Table 1111
Index | Valid?
0000 | 1
0001 | 0
0010 | 0
… | 0
1111 | 1
Page Directory
Empty sub-tables don’t need to be allocated :)

## Slide 83: 32-bit x86 Two-Level Page Tables
31
24
23
16
15
8
7
0
10-bits
PD Index
10-bits
PT Index
12-bits
Offset
Physical
Memory
CR3
Register
Page
Directory
Page
Tables

## Slide 84: 64-bit x86 Four-Level Page Tables
31
24
23
16
15
8
7
0
9-bits
PD1
Index
9-bits
PT Index
12-bits
Offset
Physical
Memory
CR3
Register
Page
Directory 3
Page
Directories 2
63
56
55
48
47
40
39
32
9-bits
PD2
Index
9-bits
PD3
Index
Page
Directories 1
Page
Tables

## Slide 85: Hybrid approach
Example: IA-32 architecture
Supports both segmentation and segmentation with paging
  Each segment can be 4 GB
  Up to 16 K segments per process
  Divided into two partitions
    First partition of up to 8 K segments are private to process (kept in local descriptor table (LDT))
    Second partition of up to 8K segments shared among all processes (kept in global descriptor table (GDT))

## Slide 86: Example: The Intel IA-32 Architecture (Cont.)
CPU generates logical address
  Selector given to segmentation unit
    Which produces linear addresses
  Linear address given to paging unit
    Which generates physical address in main memory
    Paging units form equivalent of MMU
    Pages sizes can be 4 KB or 4 MB

## Slide 87: Logical to Physical Address Translation in IA-32

## Slide 88: Intel IA-32 Segmentation

## Slide 89: Intel IA-32 Paging Architecture

## Slide 90: Don’t Forget the TLB
Multi-level pages look complicated
  And they are, but only when you have to traverse them
The TLB still stores VPN  PFN mappings
  TLB hits avoid reading/traversing the tables at all